## Slide 1: Cache Coherence in Multi-cores and Multiprocssors Mainak Chaudhuri mainakc@cse.iitk.ac.in

## Slide 2: Agenda
General architecture
Cache coherence
  Directory-based coherence protocols
Connection with GPUs
Accelerator coherence

## Slide 3: 1. General Architecture

## Slide 4: Shared memory multiprocessors
What do they look like?
  We will assume that each processor has a hierarchy of caches (possibly shared)
  We will not discuss shared memory in a time-shared single-thread computer
    A degenerate case of the following
  Shared cache (popular in CMPs)
  Private cache (popular in CMPs and SMPs)
  Distributed shared memory (popular in medium to large-scale servers)

## Slide 5: Private cache
P0
P1
P2
P3
CACHE
CACHE
CACHE
CACHE
INTERCONNECT
DRAM

## Slide 6: Tiled CMP (Hypothetical Floor-plan)
Pipeline
IL1
DL1
L2 slice
Pipeline
IL1
DL1
L2 slice
Pipeline
IL1
DL1
L2 slice
Pipeline
IL1
DL1
L2 slice
Crossbar
Mem.
Coh.
Cntr.
Mem.
Coh.
Cntr.

## Slide 7: Shared cache
P0
P1
P2
P3
CACHE
CACHE
CACHE
CACHE
INTERCONNECT
DRAM
SHARED CACHE

## Slide 8: Shared Cache CMP
Pipeline
IL1
DL1
Pipeline
IL1
DL1
Pipeline
IL1
DL1
Pipeline
IL1
DL1
Non-uniform access L2
(NUCA)
Mem.
Coh.
Cntr.
Mem.
Coh.
Cntr.

## Slide 9: Niagara Floor-plan

## Slide 10: Quad-core Sandy Bridge

## Slide 11: Shared vs. private in CMPs
Shared caches are often very large in the CMPs
  They are banked to avoid worst-case wire delay
  The banks are usually distributed across the floor of the chip on an interconnect
B
B
B
B
B
B
B
B
P
P
P
P

## Slide 12: Shared vs. private in CMPs
In shared caches, getting a block from a remote bank takes time proportional to the physical distance between the requester and the bank
  Non-uniform cache architecture (NUCA)
This is same for private caches, if the data resides in a remote cache
Shared cache may have higher average hit latency than the private cache
  Hopefully most hits in the latter will be local
Shared caches are most likely to have less misses than private caches
  Latter wastes space due to replication

## Slide 13: Distributed shared memory
P0
P1
P2
P3
CACHE
CACHE
CACHE
CACHE
INTERCONNECT
DRAM
DRAM
DRAM
DRAM

## Slide 14: 2. Cache Coherence

## Slide 15: Cache coherence
Nothing unique to multiprocessors
  Even uniprocessor computers need to worry about cache coherence
  For sequential programs we expect a memory location to return the latest value written
  For concurrent programs running on multiple threads or processes on a single processor we expect the same model to hold because all threads see the same cache hierarchy (same as shared L1 cache)
  For multiprocessors there remains a danger of using a stale value: hardware must ensure that cached values are coherent across the system and they satisfy programmers’ intuitive memory model

## Slide 16: Cache coherence: Example
Assume a write-through cache
  P0: reads x from memory, puts it in its cache, and gets the value 5 [(x, P0)=5]
  P1: reads x from memory, puts it in its cache, and gets the value 5 [(x, P0)=5, (x, P1)=5]
  P1: writes x=7, updates its cached value and memory value [(x, P0)=5, (x, P1)=7, (x, M)=7]
  P0: reads x from its cache and gets the value 5
  P2: reads x from memory, puts it in its cache, and gets the value 7 (now the system is completely incoherent) [P0=5, P1=7, P2=7]
  P2: writes x=10, updates its cached value and memory value [P0=5, P1=7, P2=10, M=10]

## Slide 17: Cache coherence: Example
Consider the same example with a writeback cache
  P0 has a cached value 5, P1 has 7, P2 has 10, memory has 5 (since caches are not write through)
  The state of the line in P1 and P2 is M while the line in P0 is clean
  Eviction of the line from P1 and P2 will issue writebacks while eviction of the line from P0 will not issue a writeback (clean lines do not need writeback)
  Suppose P2 evicts the line first, and then P1
  Final memory value is 7: we lost the store x=10 from P2

## Slide 18: What went wrong?
For write through cache
  The memory value may be correct if the writes are correctly ordered
  But the system allowed a store to proceed when there is already a cached copy
  Lesson learned: must invalidate all cached copies before allowing a store to proceed
Writeback cache
  Problem is even more complicated: stores are no longer visible to memory immediately
  Writeback order is important
  Lesson learned: do not allow more than one copy of a cache line in M state

## Slide 19: Implementations
Must invalidate all cached copies before allowing a store to proceed
  Need to know where the cached copies are
  Solution1: Never mind! Just tell everyone that you are going to do a store
    Leads to broadcast snoopy protocols
    Popular with small-scale bus-based CMPs and SMPs
    AMD Opteron implements it on a distributed network (the Hammer protocol)
  Solution2: Keep track of the sharers and invalidate them when needed
    Where and how is this information stored?
    Leads to directory-based scalable protocols

## Slide 20: Implementations
Directory-based protocols
  Maintain one directory entry per memory block
  Each directory entry contains a sharer bitvector and state bits
  Concept of home node in distributed shared memory multiprocessors
  Concept of sparse directory for on-chip coherence in CMPs

## Slide 21: Distributed shared memory
P0
P1
P2
P3
CACHE
CACHE
CACHE
CACHE
INTERCONNECT
DRAM
D
DRAM
D
DRAM
D
DRAM
D
Y
Y
Y
store r, Y
Home(Y)
Miss
INV (3a)
INV (3b)
GETX (1)
PUTX (2)

## Slide 22: Private cache
P0
P1
P2
P3
CACHE
CACHE
CACHE
CACHE
INTERCONNECT
DRAM
Dir
BW bottleneck

## Slide 23: Private cache
P0
P1
P2
P3
CACHE
CACHE
CACHE
CACHE
INTERCONNECT
DRAM
D
D
D
D
Y
store r, Y
Y
Miss
GETX (1)
INV (2b)
INV & XFER (2a)
PUTX (3)
Cache to cache transfer
Home(Y)

## Slide 24: Shared cache
P0
P1
P2
P3
CACHE
CACHE
CACHE
CACHE
INTERCONNECT
DRAM
B0
B1
B2
B3
D
D
D
D
In-cache tag-extended dir. (inclusive LLC only)
Y
Y
store r, Y
Home(Y)
GETX (1)
PUTX (2)
INV (3a)
INV (3b)
Y
Miss

## Slide 25: Shared cache
P0
P1
P2
P3
CACHE
CACHE
CACHE
CACHE
INTERCONNECT
DRAM
B0
B1
B2
B3
D
D
D
D
Sparse directory; R = #dir. entries/#private$ blocks
Y
Y
store r, Y
Home(Y)
GETX (1)
PUTX (2)
INV (3a)
INV (3b)
Y
Rx
Miss

## Slide 26: Implementations
Sparse directory
  Organized as a set-associative tagged cache of directory entries
  Responsible for keeping track of only those blocks currently in the private portion of the cache hierarchy
  Ideally, sparse directory should have number of sets equal to the number of sets in the private cache and number of ways equal to aggregate associativity of all private caches
    This is not a scalable organization
    A practically implementable sparse directory is over-provisioned by factor R to eliminate some of the conflicts

## Slide 27: Implementations
Do not allow more than one copy of a cache line in M state
  Need some form of access control mechanism
  Before a processor does a store it must take “permission” from the current “owner” (if any)
  Need to know who the current owner is
    Either a processor or main memory
  Solution1 and Solution2 apply here also

## Slide 28: Implementations
Latest value must be propagated to the requester
  Notion of “latest” is very fuzzy
  Once we know the owner, this is easy
  Solution1 and Solution2 apply here also

## Slide 29: Shared cache
P0
P1
P2
P3
CACHE
CACHE
CACHE
CACHE
INTERCONNECT
DRAM
B0
B1
B2
B3
D
D
D
D
Y
store r, Y
Home(Y)
GETX (1)
PUTX (3)
GETX (2)
Y
Rx
Miss

## Slide 30: Implementations
Invariant: if a cache block is not in M state in any processor, memory must provide the block to the requester
  Memory must be updated when a block transitions from M state to S state
  Note that a transition from M to I always updates memory in systems with writeback caches (these are normal writeback operations)
Most of the implementations of a coherence protocol deals with uncommon cases and races

## Slide 31: Shared cache
P0
P1
P2
P3
CACHE
CACHE
CACHE
CACHE
INTERCONNECT
DRAM
B0
B1
B2
B3
D
D
D
D
Y
load r, Y
Home(Y)
GET (1)
PUT (3a)
GET (2)
Y
Rx
Miss
SWB (3b)

## Slide 32: Invalidation acknowledgments
P0
P1
P2
P3
CACHE
CACHE
CACHE
CACHE
INTERCONNECT
DRAM
B0
B1
B2
B3
D
D
D
D
P1: y=1; P0: while (!y); x=1; P3: while(!x); print y;
Y
Y
store r, Y
Home(Y)
GETX (1)
PUTX (2)
INV (3a)
INV (3b)
Y
Rx
Miss
Initially:
x=0; y=0;

## Slide 33: Invalidation acknowledgments
P0
P1
P2
P3
CACHE
CACHE
CACHE
CACHE
INTERCONNECT
DRAM
B0
B1
B2
B3
D
D
D
D
P1: y=1; x=1; P3: while(!x); print y;
Y
Y
store r, Y
Home(Y)
GETX (1)
PUTX (2)
INV (3a)
INV (3b)
Y
Rx
Miss
Initially:
x=0; y=0;

## Slide 34: Invalidation acknowledgments
P0
P1
P2
P3
CACHE
CACHE
CACHE
CACHE
INTERCONNECT
DRAM
B0
B1
B2
B3
D
D
D
D
Inval. acks are needed to establish store completion
Y
Y
store r, Y
Home(Y)
GETX (1)
PUTX (2)
INV (3a)
INV (3b)
Y
Rx
Miss

## Slide 35: 2. Connection with GPUs

## Slide 36: Cache coherence in GPUs
GPUs have L1 caches private to each streaming multiprocessor and a shared L2 cache
  L1 caches are not coherent
    Why?
    Overheads of a directory-based cache coherence protocol: directory storage, network traffic, additional latency on critical path
    Which one of these overheads could be prohibitive for GPUs?
  Software must take charge of coherence
    No sharing across streaming multiprocessors: only embarrassingly parallel programs can be written
    Flavors of load and store instructions to convey to hardware whether to bypass the L1 cache

## Slide 37: Cache coherence in GPUs
Flavors of loads/stores
  Default flavor (ld.ca and st.ca) enables L1 caching
  Load/Store to global data can use the global caching flavors (ld.cg and st.cg) to disable L1 caching
    Data is cached in L2 cache only
    __ldcg(addr)
Coherence between CPU and GPU
  Usually coarse-grain (page level)
  Fine-grain coherence (block level) is limited to specialized integrated architectures e.g., Grace-Hopper

## Slide 38: Ordering of global accesses in GPUs
Flavors are not enough to enforce ordering of global loads/stores
  Example:
    T1 on SM1 executes A=1; flag=1;
    T2 on SM2 executes while (!flag); x=A+1;
    All loads/stores use global flavors
    There is no guarantee that T2 will use the new value of A because the stores A=1 and flag=1 may get reordered in the interconnect between SM1 and the respective L2 cache banks
  Need fence instructions to enforce the desired memory operation order within SM/across SM/across GPUs/across CPU-GPU
    T1 should have A=1; fence; flag=1;

## Slide 39: 4. Accelerator Coherence

## Slide 40: Accelerators
Hardware coprocessors to speed up execution of domain-specific functions
  Graphics: GPUs
  Crypto: crypto accelerators
  Floating-point arithmetic: FP coprocessors
  AI/ML accelerators
Accelerators usually operate as slaves of the main processor (aka the host processor)
  Programs annotate portions of the computation that should be off-loaded to the accelerator
  Host initiates accelerator execution

## Slide 41: Accelerators
Discrete accelerator
  Separate accelerator chip connected to the host
  Accelerator chip comes with its own cache hierarchy and memory
  Data may have to be copied explicitly or implicitly from host memory to accelerator memory before accelerator can operate on the data
  Example: GPU cards connected via PCIe bus
    DMA engines are employed to copy data from host memory to GPU memory
    Copy may be explicitly done in the program or implicitly done by the GPU driver

## Slide 42: Accelerators
Integrated accelerator
  Accelerator integrated into the host processor chip
  Accelerator can share parts of the host’s cache and memory resources
  Data copy between accelerator and host unnecessary
    Efficient fine-grain data sharing between host and accelerator possible through physically shared cache and memory
  Computationally less provisioned than discrete accelerators due to power (thermal) and area constraints

## Slide 43: Accelerators
Integrated accelerator
  Example: Integrated GPU in Intel CPUs starting from Sandy Bridge processor (2011)
    GPU shares the L3 cache, on-chip memory controllers, and main memory with the on-chip cores
    Intel’s Crystalwell processor (2013) introduced an L4 eDRAM cache of capacity up to 128 MB to support the high BW demand of the integrated GPU
      Sunset after Skylake processor due to improvements in the main three-level cache hierarchy
  Example: Integrated GPU in AMD CPUs starting from Llano family (2011)
    GPU does not share any cache with CPU cores, but shares the memory controllers and main memory

## Slide 44: Accelerator coherence
Accelerator-level parallelism (ALP): program partitioned between host CPU cores and accelerator(s)
  May have data shared between CPU cores and accelerators in read/write mode
  Requires coherence among CPU cores and accelerators
Integrated GPU with last-level cache shared with CPU
  GPU’s last-level cache is kept coherent with the CPU cores’ private caches (Intel’s implementation)
  Fully coherent hierarchy is expensive

## Slide 45: Accelerator coherence
Integrated GPU with last-level cache shared with CPU
  GPU’s last-level cache is kept coherent with the CPU cores’ private caches: GPU results should be written to GPU L3 cache before CPU can consume them
Shared CPU L3 cache
GPU L3 cache
GPU L2 caches
GPU L1 caches
C0 L2 cache
C1 L2 cache
C0 L1 cache
C1 L1 cache

## Slide 46: Accelerator coherence
Integrated GPU without shared cache
  Coherence options
    CPU caches and last-level GPU cache kept coherent by hardware: two-bit wide second-level directory to keep two L3 caches coherent
    Software coherence
Shared CPU L3 cache
GPU L3 cache
GPU L2 caches
GPU L1 caches
C0 L2 cache
C1 L2 cache
C0 L1 cache
C1 L1 cache

## Slide 47: Accelerator coherence
Integrated GPU without shared cache
  Hardware coherence: bandwidth of second-level directory could be a bottleneck
    This bottleneck is present in Intel’s integrated GPUs also, but masked under shared L3 cache bandwidth (dir. BW = L3 cache tag BW)
  Software coherence (AMD Llano)
    Before GPU starts working, relevant dirty data must be written back from CPU cache hierarchy to main memory
    GPU results must be flushed out of GPU cache hierarchy before CPU can consume them
    No guarantee of coherence if CPU and GPU simultaneously read/write from/to some shared data (same for Intel’s integrated GPUs)

## Slide 48: Accelerator coherence
Discrete GPU+CPU
  Coherence options
    Hardware coherence: cache-block grain
      Possible only if CPU and GPU are connected over a coherence-aware interconnect
      Possible only if CPU, GPU, and interconnect are manufactured by the same industry or in collaboration
      Example: Grace CPU + Hopper GPU of Nvidia (referred to as a superchip, but actually a multi-chip module)
    Hardware coherence: page-grain
    Software coherence
      Explicit copy operations done by program

## Slide 49: Accelerator coherence
Grace-Hopper coherence
  Grace CPU has a three-level fully coherent cache hierarchy
    Private L1+L2 caches per core and an L3 cache shared by CPU cores
  Hopper GPU has a two level cache hierarchy
    Private L1 data cache per SM and a shared L2 cache
    L1 data cache is locally invalidate and write-through for global stores
  Grace-Hopper coherent interconnect keeps the Grace cache hierarchy and Hopper L2 cache coherent using a high-bandwidth directory-based coherence protocol
    CPU stores do not propagate to Hopper L1 caches

## Slide 50: Accelerator coherence
Grace-Hopper coherence
  Supports acquire-release based lazy software coherence
  Acquire is a synchronization operation with the intent to read (and possibly modify) the synchronization variable
    Examples: lock acquire, flag read
  Release is a synchronization operation with the intent to write to the synchronization variable
    Example: lock release, flag write
  Acquire-release must be used to propagate CPU stores to GPUs

## Slide 51: Accelerator coherence
Grace-Hopper coherence
  Initially, x=0 and flag=0
  CPU thread: x=1; flag=1;
  GPU thread: while (!flag); use x;
    Mark “flag=1” as a release, which makes the compiler insert a fence instruction right before “flag=1” (store to x may not commit its value immediately without such a fence instruction in Grace; worse, “x=1” may commit after “flag=1”)
    Mark the read of flag in GPU thread as an acquire, which flushes the L1 cache of the SM housing the GPU thread (known as self-invalidation)
      Ensures that the reads of flag and x both will go to the Hopper L2 cache thereby entering the coherent domain

## Slide 52: Accelerator coherence
Grace-Hopper coherence (more example)
  Suppose a CPU thread and a GPU thread execute a critical section
  CPU thread: lock(L); x++; unlock(L)
  GPU thread: lock(L); x++; unlock(L)
    Mark “unlock(L)” as a release, which makes the compiler insert a fence instruction right before “unlock(L)” (ensures that store to x commits before unlock commits)
    Mark “lock(L)” in GPU thread as an acquire, which self-invalidates the L1 cache of the SM housing the GPU thread
      Ensures that the reads of L and x both will go to the Hopper L2 cache thereby entering the coherent domain

## Slide 53: Accelerator coherence
Page-grain hardware coherence in discrete GPU+CPU
  Copies of a page with RO permission can exist in CPU memory as well as GPU memory
  Store to a page from a CPU or a GPU invalidates the mapping of the page in all devices except the writer and migrates the latest copy of the page to the writer’s memory
    Fine-grain RW sharing is too costly
    Cost can be reduced by migrating only diffs and by advertising stores only at release operations
    Rich literature on page-grain coherence in shared memory multiprocessors (late 1980s to 1990s)
  May take help from OS/driver

## Slide 54: Accelerator coherence
Software coherence
  Options:
    Explicitly copy data from CPU to GPU and back (managed by application developer)
    Let the driver/OS do the copy operation triggered by faults due to CPU/GPU access to a page
    Copies are done always at a grain that is multiple of page size
    Optimization: OS/driver can infer access pattern and prefetch pages
  Fine-grain RW sharing is costly