## Slide 1: Zero Directory Eviction Victim: Unbounded Coherence Directory & Core Cache Isolation
Mainak Chaudhuri
Indian Institute of Technology Kanpur
HPCA 2021

## Slide 2: Sketch
ZeroDEV in brief
Result highlights
Introduction
ZeroDEV protocol
  Design overview
  Caching directory entries in LLC
  Handling directory eviction from LLC
Simulation infrastructure
Simulation results
Summary and future work

## Slide 3: Sketch
ZeroDEV in brief
Result highlights
Introduction
ZeroDEV protocol
  Design overview
  Caching directory entries in LLC
  Handling directory eviction from LLC
Simulation infrastructure
Simulation results
Summary and future work

## Slide 4: ZeroDEV in brief
C0
C1
C2
C3
Interconnection Network
Shared LLC Bank
Shared LLC Bank
Private
Cache(s)
Sparse
Directory Slice
Sparse
Directory Slice
B1
B1
B1
B2
B2
B3
B3
B2
B3
B1
Eviction
INV
DEV
INV
INV
DEV
Directory eviction victims (DEVs) degrade performance, inflate traffic
DEVs can be exploited by an attacker to control private cache contents of cores and mount timing-based side channel attacks [IEEE Security & Privacy 2019]
Can we design a DEV-free
coherence protocol for CMPs?
Ideally, in ZeroDEV: (i) perf. independent of directory size, (ii) private caches isolated from coherence directory eviction

## Slide 5: ZeroDEV in brief
C0
C1
C2
C3
Interconnection Network
Shared LLC Bank
Shared LLC Bank
Private
Cache(s)
Sparse
Directory Slice
Sparse
Directory Slice
B1
B1
B1
B2
B2
B3
B3
B2
B3
B1
Evict
Evict
?
?
ZeroDEV repurposes the LLC space to cache evicted directory entries while paying attention to LLC space management
On directory entry eviction from the LLC, ZeroDEV employs a novel technique to avoid generation of DEVs
All modifications are confined to uncore hardware, no change needed to software
ZeroDEV is the first fully hardwired DEV-free coherence protocol proposal for CMP
Inspired by In-Cache Coherence Info. [IEEE TC 2015] and Tiny Directory [HPCA 2017]; both use LLC for storing directory entries
Directory conflicts cannot be exploited to manipulate private cache contents and force certain future accesses to miss

## Slide 6: Result highlights
8-core/128-core CMPs running a large array of multi-threaded and multi-programmed workloads
  ZeroDEV performs within 1-2% of a well-optimized and well-provisioned baseline
  ZeroDEV maintains this performance level without any dedicated on-chip directory structure or with a significantly reduced directory size
    This is a result of eliminating DEVs and using the LLC space for caching directory entries

## Slide 7: Result highlights
ZeroDEV isolates core caches from the events surrounding directory entry eviction
  Directory evictions cannot influence private cache contents
  Directory conflicts cannot be exploited to force a future access to miss in the private cache
    This exploit is an important building block for a Prime+Probe attack involving DEVs [IEEE S&P 2019]
ZeroDEV enables a practically unbounded on-chip coherence directory that, to the core caches, appears to never evict a live entry

## Slide 8: Sketch
ZeroDEV in brief
Result highlights
Introduction
ZeroDEV protocol
  Design overview
  Caching directory entries in LLC
  Handling directory eviction from LLC
Simulation infrastructure
Simulation results
Summary and future work

## Slide 9: Introduction
Sparse directory is a set-associative tagged structure attached to each last-level cache (LLC) bank
  Each sparse directory entry tracks the location(s) of a block in the private cache hierarchy
  Sparse directory needs to be space-efficient as the private cache capacity in the CMP increases
  The number of sparse directory entries imposes an upper bound on the number of distinct blocks tracked at any point in time
    Volume of DEVs increases as directory size drops
    Important role in determining the performance

## Slide 10: Effect of DEVs on performance
Number of sparse directory entries is mentioned as a fraction of the number of blocks in the last-level private cache (L2 cache in our case)
Compared to a 1x sparse directory, performance drops by up to 20% for a sparse directory size of (1/32)x
With decreasing directory size, directory evictions create more DEVs in private cache hierarchy resulting in performance loss

## Slide 11: Sketch
ZeroDEV in brief
Result highlights
Introduction
ZeroDEV protocol
  Design overview
  Caching directory entries in LLC
  Handling directory eviction from LLC
Simulation infrastructure
Simulation results
Summary and future work

## Slide 12: ZeroDEV: design overview
C0
C1
C2
C3
Interconnection Network
Private
Cache(s)
B1
B2
Shared LLC Bank
Sparse
Directory Slice
B1
B2
B1
B2
Main
Memory
MC
B1
B2
On eviction from sparse directory, spill evicted entry into LLC space
On eviction from LLC, overwrite the copy of block in main memory to house the evicted directory entry
Can recover block from the copy resident in private cache(s)
No additional space needed to house evicted intra-socket directory entries

## Slide 13: ZeroDEV: design overview
Key observation
  A block is replicated at multiple places in memory hierarchy
    Use the copy in main memory to house live intra-socket directory entry evicted from a socket
Challenges
  Spilled directory entries increase LLC pressure
    May degrade performance if not done judiciously
  Sending intra-socket directory entries to main memory increases DRAM write and read traffic
    Need to keep this traffic inflation to minimum
  Need coherence protocol extensions

## Slide 14: Amount of spilling to LLC
A good estimate is the number of additional live directory entries required in an unbounded directory compared to 1x dir.
  Assumes existence of a 1x sparse directory so that only the excess needs to be housed in LLC
  Assumes one LLC block for one directory entry
At most 12% occupancy ≈ 2 ways in a 16-way LLC

## Slide 15: Amount of spilling to LLC
Caching directory entries in the LLC offers the attractive option of doing away with the on-chip dedicated directory array
  All directory entries would be spilled to LLC
  A 1x directory has number of entries equal to 25% of LLC blocks
    Arises from 4:1 capacity ratio of LLC to private L2 caches in our configurations
    Equivalent to 4 ways in a 16-way LLC
  Overall 4 to 6 ways to accommodate all live entries of an unbounded directory
    Assumes one LLC block for one directory entry

## Slide 16: Projected perf. loss due to spilling
Reduce LLC ways keeping access latency unchanged
Worst-case speedup observed within an app. suite
Average performance loss is within acceptable limits
Worst-case performance loss is moderate to large
Need better than naïve scheme of spilling in LLC

## Slide 17: Sketch
ZeroDEV in brief
Result highlights
Introduction
ZeroDEV protocol
  Design overview
  Caching directory entries in LLC
  Handling directory eviction from LLC
Simulation infrastructure
Simulation results
Summary and future work

## Slide 18: Scheme1: SpillAll
Shared LLC Bank
Sparse
Directory Slice
E1
Set
Index
Func.
Evict
Sets
Ways
B1
Replace & fill E1
A dir. entry spilled in LLC has state Dirty=1, Valid=0
An LLC lookup can have at most two hits
  Hits to a block and its spilled directory entry
  Reads out directory entry first and then the block
  One additional data array lookup for reads to shared blocks: lengthened critical path
Other drawback: Spilling increases LLC pressure

## Slide 19: Design space
Base
SpillAll
Increase in LLC pressure
Increase in read critical path

## Slide 20: Scheme2: FusePrivateSpillShared
Shared LLC Bank
Sparse
Directory Slice
E1
Set
Index
Func.
Evict
Sets
Ways
B1
Replace
Observation: requests to blocks in M/E state do not need the LLC block to generate response
  Must be forwarded to owner core
  Can use part of LLC block to store directory entry
  Significantly reduces LLC space pressure
Fuse private dir. entries and spill shared dir. entries
Coherence
State == M/E?
N
Y
Spill
Fuse

## Slide 21: Scheme2: FusePrivateSpillShared
Both fused and spilled dir. entries in the LLC use state Dirty=1, Valid=0
  Unused state in baseline
Part of a fused LLC block is overwritten to store directory entry
  Small number of bits overwritten: 3+log N where N is the number of cores
  Eviction of an E state block from private cache needs to send these bits to LLC
    Negligible increase in traffic
  Eviction of an M state block from private cache sends the full block to LLC, as usual

## Slide 22: Scheme2: FusePrivateSpillShared
Maintains invariant that a directory entry is present in the LLC in fused state if and only if it is tracking a block in M/E state
  A directory entry is in spilled state if and only if it is tracking a shared block
LLC lookup returns two hits in the target set
  Implies that one of the hitting entries is a spilled directory entry
  Implies that the block is in shared state
  Implies that the block can be read out and returned as response before consulting dir. Entry
  Preserves baseline critical path of reads

## Slide 23: Design space
Base
SpillAll
Increase in LLC pressure
Increase in read critical path
FPSS

## Slide 24: Scheme3: FuseAll
Shared LLC Bank
Sparse
Directory Slice
E1
Set
Index
Func.
Evict
Sets
Ways
B1
Spill only if the evicted directory entry’s corresponding block (e.g., B1) has been evicted from the LLC
  Overall LLC space overhead is very small
Major performance problem: all reads to shared blocks must be forwarded to a sharer
  LLC can’t respond: part of LLC block is overwritten
  One extra hop on critical path of shared reads
Fuse

## Slide 25: Design space
Base
SpillAll
Increase in LLC pressure
Increase in read critical path
FPSS
FuseAll

## Slide 26: Replacement-disabled directory
Caching directory entries in the LLC enables an interesting optimization
  Can design sparse directories that have no support for replacement
  At the time of allocating a new directory entry, if there is no invalid way in the target sparse directory set, just allocate in LLC
    Invalid ways are created in the sparse directory when directory entries are de-allocated from time to time
  Simplifies sparse directory arrays significantly
  ZeroDEV uses replacement-disabled sparse directories

## Slide 27: Sketch
ZeroDEV in brief
Result highlights
Introduction
ZeroDEV protocol
  Design overview
  Caching directory entries in LLC
  Handling directory eviction from LLC
Simulation infrastructure
Simulation results
Summary and future work

## Slide 28: Housing intra-socket dir. entry
A fused/spilled entry EB evicted from LLC is housed by overwriting the corresponding block B in home socket’s main memory
  Inter-socket coherence directory entry switches to “corrupted” state to record this status
    The memory block is corrupted and cannot be used to respond to requests
  B may be cached in multiple sockets creating multiple EB’s
  Must have provision to house multiple EB’s within the space allocated for B in home socket
    Achieved by partitioning B into fixed slots reserved for each socket’s EB

## Slide 29: Housing intra-socket dir. entry
Shared LLC Bank
Sparse
Directory Slice
Ep
Evict
Socket#p (sharer of block B)
Shared LLC Bank
Sparse
Directory Slice
Eq
Evict
Socket#q (sharer of block B)
Home memory
B
WB_DE
WB_DE
Sp
Sq

## Slide 30: Restricting DRAM traffic increase
Simple extension to LLC replacement policy
  Evict regular blocks first before evicting spilled or fused entries
  Lengthens directory entry residency in LLC
  Increases chance of directory entry getting de-allocated before eviction from LLC
    A directory entry is de-allocated when all copies of the corresponding block are evicted from private caches

## Slide 31: Handling socket misses
A core cache miss that cannot find the directory entry and the requested LLC block leads to a socket miss
  Sent to home socket (H) from req. socket (R)
R
H
GET/GETX/UPGRADE
Inter-socket dir. entry
in corrupted state?
Baseline flow
N
R sharer/owner?
Y
Send DE from
R’s partition
Y
PUT_DE
Intra-socket
protocol
WB_DE

## Slide 32: Handling socket misses
A core cache miss that cannot find the directory entry and the requested LLC block leads to a socket miss
  Sent to home socket (H) from req. socket (R)
R
H
GET/GETX/UPGRADE
Inter-socket dir. entry
in corrupted state?
Baseline flow
N
R sharer/owner?
Y
Send DE from
R’s partition
Y
Forward to sharer/
owner socket F
N
F
Fwd. GET/GETX
PUT/PUTX
WB_DE
The paper discusses in detail
how the situation where a forwarded
request fails to find the intra-scoket
directory entry in F is handled
New race

## Slide 33: Handling core cache evictions
Protocol extension needed if an eviction from a private cache fails to locate the intra-socket directory entry within socket
H
Full block WB?
Forward to home socket as WB
WB
Overwrite block in home memory
Y
C
LLC
Evict
Dir. entry not found
Socket R

## Slide 34: Handling core cache evictions
Protocol extension needed if an eviction from a private cache fails to locate the intra-socket directory entry within socket
H
Full block WB?
Forward to home socket as WB
Y
Get dir. entry
from home
N
GET_DE
PUT_DE
Last copy in socket?
Send block to home for possible update
Update dir.
entry in home
WB
WB_DE
If last global copy, update block
Y
N
C
LLC
Evict
Socket R
Dir. entry not found

## Slide 35: Eliminating socket-level DEVs
Socket-level directory can be maintained in a cache for performance reasons
Evictions from this cache can lead to DEVs
Two solutions
  Back up socket-level directory in home memory
    Small overhead for small socket counts
  Extend ZeroDEV to socket-level directory
    Evicted socket-level directory entry is stored in a partition of the home memory block and a bit per block records this status
    Overhead independent of socket count
See paper for details

## Slide 36: ZeroDEV: Putting it all together
Exploits replication of blocks across memory hierarchy for housing directory entries
Three schemes for accommodating in LLC
  SpillAll, FusePrivateSpillShared (FPSS), FuseAll
Extensions to LLC replacement policy and inter-socket protocol for accommodating directory entries in home memory blocks
New state in LLC block: fused/spilled
  No additional state bits needed
New state in inter-socket dir. entry: corrupted (repurposes existing state bits)

## Slide 37: Sketch
ZeroDEV in brief
Result highlights
Introduction
ZeroDEV protocol
  Design overview
  Caching directory entries in LLC
  Handling directory eviction from LLC
Simulation infrastructure
Simulation results
Summary and future work

## Slide 38: Simulation infra-structure
CPU cores
  8/128 out-of-order issue dynamically scheduled x86 cores clocked at 4 GHz (private L1$, L2$)
L3 cache
  Shared across all cores, 8/128 banks (set interleaved), 1 MB/256 KB 16-way per bank, 64B blocks, LRU
Sparse directory
  Each L3 cache bank has a sparse directory slice responsible for tracking the blocks of the bank
Main memory
  Two/Eight single-channel DDR3-2133 controllers

## Slide 39: Sketch
ZeroDEV in brief
Result highlights
Introduction
ZeroDEV protocol
  Design overview
  Caching directory entries in LLC
  Handling directory eviction from LLC
Simulation infrastructure
Simulation results
Summary and future work

## Slide 40: Selection between three schemes
Worst-case speedup observed within an app. suite
FusePrivateSpillShared scheme offers the best average perf. and best worst-case perf.
Speedup relative to baseline 1x

## Slide 41: Performance of ZeroDEV (1 socket)
Multi-grain Directory (MgD) [MICRO 2013] saves directory space by tracking 1KB private regions using one directory entry
MgD loses performance with decreasing directory size
Speedup relative to baseline 1x
ZeroDEV performs within 1-2% of baseline 1x and maintains perf. even without a directory

## Slide 42: Multi-socket results and more
Evaluated using four sockets each having eight cores
ZeroDEV operating without a sparse directory performs within 1.6% of baseline employing a 1x sparse directory
Many more results and analyses in the paper
  Study of individual application suites
  Sensitivity to LLC capacity and type of hierarchy
  Comparison with SecDir [ISCA 2019] that avoids direct generation of cross-core DEVs through partitioning of directory space into private and shared regions (can induce intra-core DEVs)
    Can lead to directory fragmentation due to partitioning

## Slide 43: Sketch
ZeroDEV in brief
Result highlights
Introduction
ZeroDEV protocol
  Design overview
  Caching directory entries in LLC
  Handling directory eviction from LLC
Simulation infrastructure
Simulation results
Summary and future work

## Slide 44: Summary and future work
Designed and evaluated the first DEV-free coherence protocol for CMPs
Enables a practically unbounded coherence directory
Core cache contents are isolated from events surrounding directory eviction
Performs within 1-2% of a well-provisioned baseline
Offers good performance even without a dedicated sparse directory structure
Future work: security analysis of ZeroDEV

## Slide 45
Thank you