## Slide 1
Characterizing Multi-threaded Applications for Designing Sharing-aware Last-level Cache Replacement Policies
Ragavendra Natarajan1, Mainak Chaudhuri2
1 Department of Computer Science and Engineering,
University of Minnesota, Twin Cities
2Department of Computer Science and Engineering,
Indian Institute of Technology Kanpur, India
Acknowledgment: Jayesh Gaur, Nithiyanandan Bashyam, Sreenivas Subramoney, Antonia Zhai
IEEE International Symposium on Workload Characterization (IISWC), September 23rd, 2013

## Slide 2: Managing shared LLC in multi-threaded applications
Shared LLC management crucial in modern CMPs
Current policies
  Mitigate cross-thread interference
  Improve intra-thread reuse
Multi-threaded applications have both intra-thread and cross-thread reuse
State-of-the-art polices not optimized for multi-thread applications
Can a “sharing-aware” replacement policy improve LLC performance of multi-threaded applications?

## Slide 3: Characterization Infrastructure
Multi2sim simulator to generate LLC access traces from multi-threaded applications
We model an 8-core CMP architecture
  8-way, 32KB per-core I-L1 and D-L1 caches
  8-way, 128KB per-core L2 cache
  16-way, inclusive, shared LLC
4MB and 8MB LLC capacities evaluated (4MB results in paper)
Applications from PARSEC, SPLASH and SPECOMP benchmark suites
Offline LLC model uses traces as input to generate statistics

## Slide 4: How important is cross-thread reuse in multi-threaded applications?
Shared fills form a significant fraction of useful LLC fills.
Three categories of LLC fills:
  No-reuse fills
  Private-reuse fills  Intra-thread reuse
  Shared fills  Cross-thread reuse
Useful LLC fills
Chart: Distribution of LLC fills with Belady’s optimal policy
| canneal | dedup | ferret | fluidanimate | freqmine | raytrace | streamcluster | vips | equake | art | radix | fft | ocean | AVERAGE
Shared | 0.39646 | 0.37823 | 0.4994 | 0.1148 | 0.14886 | 0.24784 | 0.19388 | 0.5054 | 0.098951 | 0.037888 | 0.020333 | 0.034671 | 0.0055315 | 0.20633
Private-reuse | 0.018772 | 0.026742 | 0.16566 | 0.35539 | 0.26721 | 0.048643 | 0.43926 | 0.23198 | 0.89457 | 0.84572 | 0.27728 | 0.027643 | 0.1761 | 0.29038
No-reuse | 0.58477 | 0.59503 | 0.33494 | 0.52982 | 0.58392 | 0.70352 | 0.36686 | 0.26262 | 0.00648 | 0.1164 | 0.70238 | 0.93769 | 0.81837 | 0.50329

## Slide 5: How important is cross-thread reuse? (contd.)
Shared LLC fills are more valuable compared to private fills in multi-threaded applications.
Chart: Reuse count per shared LLC fill normalized to reuse count per private LLC fill with Belady’s optimal policy
| canneal | dedup | ferret | fluidanimate | freqmine | raytrace | streamcluster | vips | equake | art | radix | fft | ocean | AVERAGE
8MB LLC | 1.9382 | 16.7746 | 3.4777 | 2.2122 | 3.9957 | 2.4414 | 4.4565 | 4.5927 | 2.3071 | 2.9201 | 1.6049 | 0.37606 | 2.2116 | 2.7214

## Slide 6: How sharing-aware are current replacement policies?
All LLC replacement policies have some inherent sharing-awareness
LLC replacement policy can significantly affect data sharing in LLC
  Belady’s optimal policy  maximum data sharing
  Realistic policies  less data sharing
Policies evaluated: LRU, SRRIP & DRRIP (ISCA 2010), SHiP-PC (MICRO 2011), SA-Partition (IPDPS 2009)
Metrics for quantifying sharing-awareness of a replacement policy
  Fraction of shared LLC fills
  Average number of distinct sharers per LLC fill

## Slide 7: How sharing-aware are current replacement policies? (contd.)
Fraction of shared fills in existing policies significantly smaller than Belady’s optimal policy
Chart: Number of private and shared fills normalized to Belady’s optimal policy
| Belady | LRU | SRRIP | DRRIP | SHiP-PC | SA-Partition
Shared LLC Fills | 0.20633 | 0.26051 | 0.19049 | 0.15364 | 0.14786 | 0.14882
Private LLC Fills | 0.79367 | 1.6215 | 1.3304 | 1.3171 | 1.2165 | 1.3617

## Slide 8: How sharing-aware are current replacement policies? (contd.)
Large gap between sharing-awareness of current policies and optimal sharing-awareness
Chart: 
| Belady | LRU | SRRIP | DRRIP | SHiP-PC | SA-Partition
Average # of sharers per LLC fill | 1.4751 | 1.2742 | 1.27 | 1.2422 | 1.2612 | 1.2254

## Slide 9: What is the potential improvement with sharing-aware policies?
Two oracle policies to evaluate potential improvement: Oone and Oall
Oracle policies augment replacement policy with optimal sharing information
Oracles use annotated LLC access trace to get sharing information
LLC access trace
DR c0 0xabcdef80
ST c1 0x34567880
CR c0 0x12786440
…
…
Annotated LLC access trace
DR c0 0xabcdef80
LLC miss; evicting 0x56234240
ST c1 0x34567880
CR c0 0x12786440
LLC miss; evicting 0xabcdef80
…
…
Optimal lifetime of
0xabcdef80

## Slide 10: Sharing-aware oracles: Augmenting sharing information
LLC fill
Accessed by >1 core before end of current optimal LLC lifetime?
YES
NO
Mark as shared in LLC and record number of sharers
Do not mark as shared

## Slide 11: Sharing-aware oracles: Updating sharing information
LLC hit
Access from new sharer?
YES
NO
Oone oracle?
Clear shared bit
YES
NO
# sharers = optimal sharer count? (Oall oracle)
YES
Don’t change shared bit
NO

## Slide 12: Sharing-aware oracles: Making sharing-aware replacement decisions
LLC eviction
All cache blocks in set marked shared?
YES
NO
Clear shared bits of all blocks
Choose victim from unmarked cache blocks

## Slide 13: What is the potential improvement with sharing-aware policies?
Chart: Normalized LLC misses
| canneal | dedup | ferret | fldanmt | freqmine | raytrace | strclstr | vips | equake | art | radix | fft | ocean | AVG
LRU Oone | 0.9194 | 0.95581 | 0.8985 | 0.97518 | 0.92567 | 0.90643 | 0.96477 | 0.72917 | 1 | 1 | 0.99305 | 0.99148 | 0.99613 | 0.94274
DRRIP Oone | 0.92297 | 0.94382 | 0.90547 | 0.97796 | 0.92364 | 0.94216 | 0.87519 | 0.8016 | 1 | 0.99987 | 0.98604 | 0.99428 | 0.99461 | 0.94366
SHIP-PC Oone | 0.96 | 0.94388 | 0.91289 | 0.9866 | 0.93108 | 0.9519 | 1.0273 | 0.92702 | 1 | 1.0003 | 0.99654 | 0.99849 | 0.99501 | 0.97161
LLC misses incurred by sharing-aware oracles normalized to corresponding baseline policies

## Slide 14: What is the potential improvement with sharing-aware policies?
Oone and Oall reduce LLC misses across all policies
Chart: Normalized LLC misses
| canneal | dedup | ferret | fldanmt | freqmine | raytrace | strclstr | vips | equake | art | radix | fft | ocean | AVG
LRU Oall | 0.7641 | 0.91496 | 0.7909 | 0.97462 | 0.91846 | 0.83595 | 0.9577 | 0.59284 | 1 | 0.99887 | 0.99305 | 0.99128 | 0.9961 | 0.90222
DRRIP Oall | 0.91754 | 0.92165 | 0.83251 | 0.98175 | 0.91764 | 0.87842 | 0.86942 | 0.7361 | 0.99306 | 0.99985 | 0.98628 | 0.99434 | 0.99474 | 0.92487
SHIP-PC Oall | 0.90816 | 0.92414 | 0.84682 | 0.98658 | 0.92549 | 0.90652 | 1.0155 | 0.82097 | 1 | 1.0007 | 0.99652 | 0.99849 | 0.99501 | 0.94807
LLC misses incurred by sharing-aware oracles normalized to corresponding baseline policies

## Slide 15: What are the challenges in realizing sharing-aware replacement policies?
Realistic implementations of oracles need fill time information
  Is the cache block likely to be shared during its optimal LLC lifetime?
  If shared, then how many sharers?
An LLC fill-time sharing behavior predictor can answer these questions
Characterize multi-threaded applications to answer the following questions:
  How is data shared in multi-threaded applications?
  How predictable is data sharing in multi-threaded applications?

## Slide 16: How is data shared in multi-threaded applications?
Data sharing depends on multiple factors
  Application characteristics
  LLC replacement policy
  LLC capacity
Cache block shared at LLC level if it is shared in at least one LLC lifetime
LLC lifetime sharing: Amount of data sharing for a given LLC configuration
Program level sharing
  Maximum possible sharing with an infinite LLC
  Application characteristic and independent of LLC size

## Slide 17: How is data shared in multi-threaded applications? (contd.)
  LLC data sharing is sparse. Policies that capture program level sharing will be ineffective (SA-Partition)
Chart: Fraction of cache blocks
| canneal | dedup | ferret | fluidanimate | freqmine | raytrace | streamcluster | vips | equake | art | radix | fft | ocean | AVG
Program level | 0.94451 | 0.60199 | 0.88666 | 0.1546 | 0.40149 | 0.85177 | 0.98142 | 0.83392 | 0.098951 | 0.068016 | 0.92777 | 0.58459 | 0.014701 | 0.56541
LLC lifetime level | 0.49655 | 0.5674 | 0.7986 | 0.15434 | 0.27045 | 0.4124 | 0.97597 | 0.76678 | 0.098951 | 0.067831 | 0.10527 | 0.090611 | 0.014584 | 0.37075

## Slide 18: How predictable is data sharing in multi-threaded applications?
A cache block can be private or shared in each of its LLC lifetimes
Sharing behavior can be represented by a binary string (sharing history)
  0x34239840 P S P S P S . . .
Chart: Distribution of shared cache blocks based on LLC lifetime sharing with Belady’s optimal policy
| canneal | dedup | ferret | fldanmt | freqmine | raytrace | stclstr | vips | equake | art | radix | fft | ocean | AVERAGE
< 50% of LLC lifetimes | 0.55845 | 0.53084 | 0.36611 | 0.010013 | 0.43701 | 0.16329 | 0.54242 | 0.13935 | 0 | 0.0039828 | 0.83463 | 0.92724 | 0.72894 | 0.40325
50% - 90% of LLC lifetimes | 0.36521 | 0.33686 | 0.54659 | 0.38049 | 0.44515 | 0.3447 | 0.020388 | 0.47455 | 0.011491 | 0.13353 | 0.15922 | 0.068745 | 0.18347 | 0.26695
> 90% of LLC lifetimes | 0.076343 | 0.13229 | 0.087299 | 0.6095 | 0.11783 | 0.49201 | 0.43719 | 0.3861 | 0.98851 | 0.86249 | 0.0061501 | 0.0040144 | 0.087589 | 0.32979
LLC data sharing is irregular

## Slide 19: How predictable is data sharing? (contd.)
Explore feasibility of designing sharing behavior predictors
History-based sharing behavior predictors predict sharing behavior based on history window of last w LLC lifetimes
0x34239840 P S P S P S . . .
Predictability score of address A defined as:
PA =
Similarly define predictability score for load/store PC
PA close to 1 indicates good predictability (0.5 ≤ PA ≤ 1)
Most addresses and PCs have short (< 5) lifetimes
Pattern | # P | # S
PP | 0 | 0
PS | 2 | 0
SP | 0 | 2
SS | 0 | 0

## Slide 20: How predictable is data sharing? (contd.)
Sharing behavior does not correlate well with sharing history of shared block addresses
Chart: Distribution of shared addresses based on predictability index (2-bit history)
| canneal | dedup | ferret | fluidanimate | freqmine | raytrace | streamcluster | vips | AVERAGE
0.5 - 0.6 | 0.087168 | 0.55554 | 0.24027 | 0.59456 | 0.67533 | 0.83105 | 0.41205 | 0.785 | 0.52262
0.6 - 0.9 | 0.53038 | 0 | 0.40874 | 0.0061073 | 4.7816e-05 | 0 | 0.11459 | 0.056955 | 0.1396
> 0.9 | 0.38245 | 0.44446 | 0.35099 | 0.39933 | 0.32462 | 0.16895 | 0.47336 | 0.15804 | 0.33778

## Slide 21: How predictable is data sharing? (contd.)
Sharing behavior does not correlate well with sharing history of LLC fill PCs
Evaluation of sharing predictors with DRRIP and SHIP-PC policies leads to negligible improvements
Chart: Distribution of LLC fill PCs based on predictability index (2-bit history)
| canneal | dedup | ferret | fluidanimate | freqmine | raytrace | streamcluster | vips | AVERAGE
0.5 - 0.6 | 0.65 | 0.38281 | 0.40806 | 0.41579 | 0.49278 | 0.5 | 0.36232 | 0.38838 | 0.45002
0.6 - 0.9 | 0.14167 | 0.24219 | 0.25161 | 0.10526 | 0.11959 | 0.41026 | 0.14493 | 0.39201 | 0.22594
> 0.9 | 0.20833 | 0.375 | 0.34032 | 0.47895 | 0.38763 | 0.089744 | 0.49275 | 0.2196 | 0.32404
High-level program semantic information may help design sharing-aware policies

## Slide 22: Summary
Cross-thread reuse is critical in multi-threaded applications
Current policies not optimized for multi-threaded applications
Sharing-aware policies can significantly improve multi-threaded applications
Sharing-aware policies require a sharing behavior predictor in conjunction with baseline replacement policy
Sharing-aware policies must look beyond address and fill PC based predictors
High-level program semantic information can help design sharing-aware replacement policies

## Slide 23: BACKUP

## Slide 24: LLC hits to private and shared cache blocks
Chart: Fraction of LLC hits to private and shared cache blocks
| canneal | dedup | ferret | fluidanimate | freqmine | raytrace | streamcluster | vips | equake | art | radix | fft | ocean | AVERAGE
Shared | 0.97615 | 0.9958 | 0.91292 | 0.41677 | 0.69002 | 0.92559 | 0.66296 | 0.90914 | 0.20331 | 0.11568 | 0.10529 | 0.32051 | 0.064957 | 0.56147
Private | 0.023847 | 0.0041972 | 0.087078 | 0.58323 | 0.30998 | 0.074411 | 0.33704 | 0.090862 | 0.79669 | 0.88432 | 0.89471 | 0.67949 | 0.93504 | 0.43853

## Slide 25: How sharing-aware are current replacement policies? (contd.)
Chart: Number of private and shared fills normalized to Belady’s optimal policy
4
B
L
S
D
SH
SP
Fraction of shared fills in existing policies significantly smaller than Belady’s optimal policy

## Slide 26: How sharing-aware are current replacement policies? (contd.)
Chart: Average number of distinct sharers per LLC fill
| canneal | dedup | ferret | fluidanimate | freqmine | raytrace | streamcluster | vips | equake | art | radix | fft | ocean | AVG
Belady | 2.0013 | 2.0887 | 2.137 | 1.1531 | 1.3759 | 1.3997 | 1.2937 | 2.302 | 1.1232 | 1.2369 | 1.0217 | 1.0362 | 1.0075 | 1.4751
LRU | 1.614 | 2.0039 | 1.4582 | 1.1532 | 1.229 | 1.1606 | 1.1194 | 1.5126 | 1.1232 | 1.1805 | 1.0023 | 1.0013 | 1.0066 | 1.2742
SRRIP | 1.5073 | 1.9385 | 1.4596 | 1.1289 | 1.2301 | 1.1617 | 1.1364 | 1.678 | 1.1232 | 1.138 | 1.0029 | 1.0013 | 1.0041 | 1.27
DRRIP | 1.2532 | 1.9218 | 1.4496 | 1.0815 | 1.2272 | 1.2005 | 1.1145 | 1.6643 | 1.0864 | 1.1354 | 1.0032 | 1.0083 | 1.003 | 1.2422
SHiP - PC | 1.337 | 1.9098 | 1.4336 | 1.1012 | 1.2296 | 1.2097 | 1.1373 | 1.7271 | 1.1232 | 1.1577 | 1.0156 | 1.0103 | 1.0037 | 1.2612
SP | 1.2228 | 1.8421 | 1.4278 | 1.0678 | 1.2249 | 1.1636 | 1.113 | 1.5978 | 1.1232 | 1.1377 | 1.0031 | 1.0035 | 1.0033 | 1.2254
Large gap between sharing-awareness of current policies and optimal sharing-awareness