## Slide 1: Zero Inclusion Victim (ZIV): Isolating Core Caches from Inclusive Last-level Cache Evictions
Mainak Chaudhuri
Indian Institute of Technology Kanpur
ISCA 2021

## Slide 2: Sketch
ZIV LLC in brief
Result highlights
Introduction
ZIV LLC design
  Finding relocation sets
  Replacement policy in relocation sets
  Managing relocated blocks
Simulation infrastructure
Simulation results
Summary and future work

## Slide 3: Sketch
ZIV LLC in brief
Result highlights
Introduction
ZIV LLC design
  Finding relocation sets
  Replacement policy in relocation sets
  Managing relocated blocks
Simulation infrastructure
Simulation results
Summary and future work

## Slide 4: ZIV LLC in brief
C0
C1
C2
C3
Interconnection Network
Shared LLC Bank
Shared LLC Bank
Private
Cache(s)
Sparse
Directory Slice
Sparse
Directory Slice
B1
B1
B1
B2
B2
B3
B3
E1
Eviction
INV
IV
INV
INV
IV
E2
E3
Inclusion victims (IVs) increase private cache and LLC misses, degrade performance, inflate traffic
Perf. loss is a function of private cache capacity and LLC policy; LLC policies approaching Belady’s MIN suffer most
IVs make LLC eviction-based timing side channel attacks much less noisy because IVs can be used to control private cache contents of cores through LLC eviction
IVs rule out the use of large private caches, particularly large private L2 caches
IVs are not fundamental to the inclusion property, but arise due to the way the inclusive LLC contents are managed
Can we design an inclusive LLC that is guaranteed to never generate IVs?
Zero Inclusion Victim (ZIV) LLC

## Slide 5: ZIV LLC in brief
C0
C1
C2
C3
Interconnection Network
Shared LLC Bank
Shared LLC Bank
Private
Cache(s)
Sparse
Directory Slice
Sparse
Directory Slice
B1
B1
B1
B2
B2
B3
B3
E1
Eviction
E2
E3
RS
Relocate
PTR
Relocate
PTR
RS
Challenge#1: Efficiently find a relocation set (RS) that has at least one block with no privately cached copy (basic ZIV)
Such a relocation set is guaranteed to exist because inclusive LLC capacity is more than aggregate private cache capacity
Challenge#2: Efficiently manage accesses to and replacement of relocated blocks
Challenge#3: Efficiently find a “good” relocation set to make global victim choices high-performance (performant ZIV)
Key goals: (i) perf. close to non-inclusive LLC, (ii) large L2 cache with inclusive LLC, (iii) energy- and area-efficient relocation
ZIV LLC is the first inclusive LLC design that guarantees freedom from IVs and isolates core caches from inclusive LLC evictions

## Slide 6: Result highlights
Evaluated on 8-core/128-core CMPs with multi-threaded and multi-programmed workloads
  ZIV LLC performs close to a non-inclusive LLC for different types of LLC replacement policies
    We study LRU and Hawkeye policies
  ZIV LLC gracefully supports private L2 caches with capacity up to half the LLC capacity
  ZIV LLC comfortably outperforms related proposals such as QBS [MICRO 2010] and SHARP [ISCA 2017]
    Performance lead grows with increasing L2 cache capacity

## Slide 7: Result highlights
ZIV LLC retains all benefits of an inclusive LLC
  Much simpler cache coherence than non-inclusive cache hierarchy
With ZIV LLC, private cache contents cannot be manipulated through LLC evictions
  No inclusion victim

## Slide 8: Sketch
ZIV LLC in brief
Result highlights
Introduction
ZIV LLC design
  Finding relocation sets
  Replacement policy in relocation sets
  Managing relocated blocks
Simulation infrastructure
Simulation results
Summary and future work

## Slide 9: Why inclusive LLC
Significantly simplified cache coherence in a chip-multiprocessor with inclusive LLC
Private cache miss request
Sparse
Directory
Slice
Last-level Cache Bank
Hit
Hit
Miss
Hit
Miss
Miss
Hit
Miss
Not possible
Coher. prot.
LLC resp.
Socket resp.
The fourth case can arise in non-inclusive designs, is far more complex than the other three cases, and introduces new transient states and new protocol races

## Slide 10: Performance loss in inclusive LLC
Evaluated on 8-core CMP with 72 multi-prog. workloads
Normalized to I-LRU (LLC policy) with 256 KB L2 cache
I-LRU vs. NI-LRU: Perf. gap increases with increasing L2 cache capacity due to increasing volume of IVs
I-Hawkeye vs. NI-Hawkeye: Much bigger perf. gap; very big perf. loss in some of the workloads with I-Hawkeye
Performance loss increases steeply as LLC replacement policy approaches Belady’s MIN

## Slide 11: Sketch
ZIV LLC in brief
Result highlights
Introduction
ZIV LLC design
  Finding relocation sets
  Replacement policy in relocation sets
  Managing relocated blocks
Simulation infrastructure
Simulation results
Summary and future work

## Slide 12: Block relocation flow
Has privately cached copies?
LLC fill port
arbiter
nextRS
New LLC fill
Target LLC set
Sparse Dir.
Slice
Evict
Consult on-chip dir.
N
Evict & STOP
Y
Relocation FIFO
Next relocation set
LLC victim with no
privately cached copy

## Slide 13: Finding relocation sets
Relocation sets need to satisfy certain properties
  Two such properties are: Does the set have an invalid way? Does the set have a valid block with no privately cached copy?
    Invalid property and NotInPrC property
  Attach property bits to each LLC set to identify such sets
LLC set
NotInPrC
Invalid
Any invalid way?
Any block with no
privately cached copy?

## Slide 14: Finding relocation sets
NotInPrC PV
Invalid PV
LLC set
Property
Vectors (PVs)
nextRS
nextRS
Register nextRS of each PV points to the next round-robin position (with wrap-around) in PV with a set bit
If Invalid PV is not empty, use its nextRS as the reloc. set index; otherwise use nextRS of NotInPrC PV

## Slide 15: Efficiently computing nextRS
It is possible to efficiently compute decoded nextRS from the decoded current RS and PV
nextRS
Decoder
00000000001000000
Wordlines
Decoded nextRS
We will directly compute decoded nextRS from a given PV and decoded RS

## Slide 16: Efficiently computing nextRS
00000000001000000
Decoded
RS
11111111110000000
Gen.
mask
mask
00101101001110010
PV
00101101000000000
upperPV
& mask
11010011000000000
2’s compl.
upperPV
&
00000001000000000
Decoded
nextRS

## Slide 17: Efficiently computing nextRS
00000000001000000
Decoded
RS
00000000000111111
Gen.
mask
mask
00000000001110010
PV
upperPV=0
00000000000110010
lowerPV
& mask
11111111111001110
2’s compl.
lowerPV
&
00000000000000010
Decoded
nextRS

## Slide 18: Finding “good” relocation sets
Invalid and NotInPrC properties may not offer “good” relocation sets
  Need to combine with locality-centric properties
LRUNotInPrC property: a set in which the LRU block does not have any privately cached copy (applicable if LLC policy is LRU)
  Needs a third PV in addition to Invalid and NotInPrC PVs to find a relocation set
    If Invalid PV is not empty, use its nextRS
    If Invalid PV is empty and LRUNotInPrC PV is not empty, use the nextRS of LRUNotInPrC PV
    Use the nextRS of NotInPrC PV if other two PVs empty

## Slide 19: Finding “good” relocation sets
MaxRRPVNotInPrC property: a set in which the block with max RRPV does not have any privately cached copy (applicable if LLC policy uses RRPV or other non-LRU age)
  Needs a third PV in addition to Invalid and NotInPrC PVs to find a relocation set
  Algorithm to find relocation sets is similar to LRUNotInPrC

## Slide 20: Finding “good” relocation sets
LikelyDeadNotInPrC property: a set having a likely dead block with no privately cached copy
  Agnostic to LLC policy, but needs to identify likely dead blocks having no privately cached copies
    Appeals to Cache Hierarchy-aware Replacement (CHAR) proposal [PACT 2012]
    Infers liveness of blocks evicted from private caches
    See paper for details
  Needs a third PV for LikelyDeadNotInPrC
  Priority order of nextRS: Invalid PV, LikelyDeadNotInPrC PV, NotInPrC PV

## Slide 21: Finding “good” relocation sets
MaxRRPVLikelyDeadNotInPrC property: LikelyDeadNotInPrC property applied to LLC employing RRPV-based policy
  Needs four PVs: Invalid, NotInPrC, LikelyDeadNotInPrC, MaxRRPVNotInPrC
  Priority order for nextRS: Invalid, MaxRRPVNotInPrC, LikelyDeadNotInPrC, NotInPrC
Reduce the number of relocations
  In all cases, at each priority level, the original LLC set is checked to see if it satisfies the property of that level; if yes, no relocation

## Slide 22: Critical path and area estimates
RTL synthesis of decoded nextRS computation using 45 nm TSMC process
Critical path meets a 0.75 ns timing target for a fully combinational implementation
  Three-cycle latency and repeat interval @ 4 GHz clock frequency
Area overhead per LLC bank
  Properties requiring two PVs: 0.045 mm2
  Properties requiring three PVs: 0.078 mm2
  Properties requiring four PVs: 0.099 mm2

## Slide 23: Sketch
ZIV LLC in brief
Result highlights
Introduction
ZIV LLC design
  Finding relocation sets
  Replacement policy in relocation sets
  Managing relocated blocks
Simulation infrastructure
Simulation results
Summary and future work

## Slide 24: Replacement policy in RS
A relocation set is found by following a certain priority order among the set properties
Replacement policy in a relocation set follows the same priority order to identify the victim
Consider the LikelyDeadNotInPrC property
  Implemented using three PVs with priority order (highest to lowest): Invalid, LikelyDeadNotInPrC, NotInPrC
  Replacement policy in the RS evicts an invalid way (if any), next the likely dead block closest to the LRU position, and finally the NotInPrC block closest to the LRU position

## Slide 25: Sketch
ZIV LLC in brief
Result highlights
Introduction
ZIV LLC design
  Finding relocation sets
  Replacement policy in relocation sets
  Managing relocated blocks
Simulation infrastructure
Simulation results
Summary and future work

## Slide 26: Managing relocated blocks
Each LLC block has a new Relocated state to identify the relocated blocks
  LLC hit = valid && !Relocated && tag match
Each sparse directory entry also has a new Relocated state in addition to a pointer field for recording the location of a relocated block
  Pointer field records (bank id, LLC set, LLC way)

## Slide 27: Accessing a relocated block
Private cache miss request
LLC tag
Sparse Dir.
Slice
R
Miss
LLC data
Data block
PTR
Critical path length = max (dir. array, LLC tag array) + LLC data array
Baseline critical path length = LLC tag array + LLC data array
ZIV LLC latency is 1-3 cycles higher for relocated block access

## Slide 28: Storage overhead
Three new state bits per LLC block
  Relocated, NotInPrC, LikelyDead
  6 KB per 1 MB LLC bank
One new state bit and a pointer per sparse directory entry
  18 KB, 36 KB, 54 KB per LLC bank in a 2x directory for 256 KB, 512 KB, 768 KB L2 cache configurations
Overall, 24 KB to 60 KB per 1 MB LLC
  Under 6% overhead

## Slide 29: Sketch
ZIV LLC in brief
Result highlights
Introduction
ZIV LLC design
  Finding relocation sets
  Replacement policy in relocation sets
  Managing relocated blocks
Simulation infrastructure
Simulation results
Summary and future work

## Slide 30: Simulation infrastructure
CPU cores
  8 out-of-order issue dynamically scheduled x86 cores clocked at 4 GHz (private L1$, L2$)
    32 KB 8-way L1 caches
    256 KB 8-way, 512 KB 8-way, 768 KB 12-way L2 cache
    L2 cache lookup latency: 4, 5, 6 cycles
L3 cache
  1 MB/2 MB 16-way per bank, 64B blocks, LRU or Hawkeye, 7/8 cycles lookup latency
Main memory
  Two single-channel DDR3-2133 controllers
See paper for 128-core evaluation of TPC-E

## Slide 31: Sketch
ZIV LLC in brief
Result highlights
Introduction
ZIV LLC design
  Finding relocation sets
  Replacement policy in relocation sets
  Managing relocated blocks
Simulation infrastructure
Simulation results
Summary and future work

## Slide 32: Simulation results: LRU policy
The ZIV LLC design using the LikelyDead property surpasses or meets the NI LLC perf.
QBS, SHARP, and the basic ZIV LLC designs fail to scale up perf. with L2 cache capacity
Quality of global victims grows in importance for ZIV LLC perf. with increasing L2$ capacity
1 MB LLC/core

## Slide 33: Simulation results: Hawkeye policy
The ZIV LLC design using the LikelyDead property comes close to the NI LLC perf. and scales gracefully up to 512 KB L2 cache size
1 MB LLC/core

## Slide 34: Simulation results: Bigger LLC
2 MB LLC/core, 1 MB L2 cache/core
The ZIV LLC design using the LikelyDead property continues to offer performance close to the NI LLC design

## Slide 35: Simulation results: Reloc. stats
Hawkeye policy
LRU policy
Hawkeye policy experiences more number of shorter inter-relocation intervals
A negligible fraction of inter-relocation intervals has length less than 5 cycles

## Slide 36: Simulation results: EPI
Average EPI contribution is at most 12 pJ arising from block relocation and wider dir.
This EPI addition is more than compensated by savings in the cache hierarchy and DRAM

## Slide 37: Sketch
ZIV LLC in brief
Result highlights
Introduction
ZIV LLC design
  Finding relocation sets
  Replacement policy in relocation sets
  Managing relocated blocks
Simulation infrastructure
Simulation results
Summary and future work

## Slide 38: Summary and future work
Future work: better global victim selection, security analysis
Inclusive LLC
Big core caches
No inclusion victim
Performance close to non-inclusive LLC
Simplicity of cache coherence as in inclusive hierarchy
A happy family of on-chip caches
ZIV LLC

## Slide 39: Zero Inclusion Victim (ZIV): Isolating Core Caches from Inclusive Last-level Cache Evictions
Mainak Chaudhuri
Indian Institute of Technology Kanpur
ISCA 2021
Thank you
Celebrating half a century of microprocessors