## Slide 1: Efficient Management of LLCs in GPUs for 3D Scene Rendering Workloads
Jayesh Gaur (Intel)
Raghuram Srinivasan (Ohio State)
Sreenivas Subramoney (Intel)
Mainak Chaudhuri (IIT, Kanpur)

## Slide 2: Sketch
Talk in one slide
Result highlights
Understanding the potential
Reuses in 3D graphics data
Our policy proposals
Evaluation methodology
Simulation results
Summary

## Slide 3: Sketch
Talk in one slide
Result highlights
Understanding the potential
Reuses in 3D graphics data
Our policy proposals
Evaluation methodology
Simulation results
Summary

## Slide 4: Talk in One Slide
3D scene rendering pipeline generates accesses to different types of data
  Vertex, vertex index, depth, hierarchical depth, stencil, render targets (same as pixel colors), and textures for sampling
  GPUs include small render caches for each such data type and more recently read/write last-level caches (LLCs) shared by all such data streams
Our proposal: graphics stream-aware probabilistic caching (GSPC) for GPU LLC
  Learns inter- and intra-stream reuse probabilities from a few sample LLC sets and modulates insertion/promotion in other sets

## Slide 5: Result highlights
Three increasingly better policies coupled with uncached displayable color data
  Baseline: two-bit DRRIP
  Workloads: 52 DirectX frames selected from eight game titles and four benchmark applications using Direct3D 10 and 11 APIs
  LLC miss saving: up to 29.6% and on average 13.1% with an 8 MB 16-way LLC
  Frame rate improvement: up to 18.2% and on average 8.0%; with increasing LLC capacity, it gets even better (11.8% with a 16 MB LLC)
  More important as GPUs get more aggressive

## Slide 6: Sketch
Talk in one slide
Result highlights
Understanding the potential
Reuses in 3D graphics data
Our policy proposals
Evaluation methodology
Simulation results
Summary

## Slide 7: Characterization framework
Functional LLC model
  8 MB 16-way 64-byte blocks
  Digests LLC access traces collected from a detailed timing simulator of a high-end GPU
Load/Store trace collection
  52 frames are selected from twelve DirectX applications that use Direct3D 10 and 11 APIs
    Eight games and four benchmark applications
  All Direct3D APIs are intercepted in each frame and replayed through the detailed simulator
  All LLC accesses are logged in a trace
  The modeled LLC is non-inclusive/non-exclusive

## Slide 8: GPU last-level cache interface
RENDERING PIPELINE
VTX
VTX IDX
HIZ
Z
TEX
RT/CLR
STC
GPU LLC
DRAM
Belady’s optimal policy projects a 36.6% average saving in LLC misses compared to two-bit DRRIP
Large potential for improving system bandwidth, power, and performance

## Slide 9: LLC accesses
LLC accesses arise due to misses in the GPU render caches
  For example, a sampler request comes to the LLC only if the access has missed in all levels of the texture cache hierarchy of the GPU
The LLC accesses can be partitioned based on the source of the request
  Each such partition will be referred to as a 3D graphics stream
  We consider eight streams: Vertex, HiZ, Z, render target (RT), texture sampler (TEX), stencil (STC), displayable color, and the rest (shader code, constants, etc.)

## Slide 10: LLC access traffic
Which 3D graphics streams are important?
TEX 34%
RT 40%
Z 10%
Most LLC accesses touch texture sampler data, render targets (pixel colors), and depth
HiZ 7%
VTX 4%
REST 5%

## Slide 11: LLC read hit rates (8 MB 16-way)
Texture sampler data
  Belady’s optimal: 53.4%
  Two-bit DRRIP: 22.0%
  Single-bit NRU: 18.4%
Render targets
  Belady’s optimal: 59.8%
  Two-bit DRRIP: 50.1%
  Single-bit NRU: 41.5%
Depth
  Belady’s optimal: 77.1%
  Two-bit DRRIP: 58.0%
  Single-bit NRU: 58.0%
LLC hits arise from render to texture reuses and intra-stream texture reuses
LLC hits arise from intra-stream render target blend ops
LLC hits arise from intra-stream depth reuses
Texture sampler data presents the largest opportunity for improvement

## Slide 12: Sketch
Talk in one slide
Result highlights
Understanding the potential
Reuses in 3D graphics data
Our policy proposals
Evaluation methodology
Simulation results
Summary

## Slide 13: LLC reuse study#1: Texture
LLC hits enjoyed by the texture samplers come from two sources
Inter-stream reuses
  A previously created render target block is consumed by the texture samplers from the LLC
  Arises from a technique called render to texture, very popular for generating dynamic textures that need to be updated on a per-frame basis
  Examples include waves, moving clouds, foliage, fluttering cloth, smoke, fire, and many more
Intra-stream reuses
  A texture block, previously used by the samplers, is reused by the samplers from the LLC

## Slide 14: LLC reuse study#1: Texture
Distinguishing inter-stream reuses from intra-stream reuses
  Attach one bit with each LLC block; call it RT bit
  All LLC blocks accessed/filled by the render target stream have the RT bit set
  A texture sampler access that consumes an LLC block with the RT bit set is identified as an inter-stream reuse; the RT bit gets reset at this point
  All other texture sampler hits in the LLC are classified as intra-stream reuses

## Slide 15: LLC reuse study#1: Texture
Out of all LLC hits enjoyed by the texture sampler accesses in Belady’s optimal policy
  Inter-stream: 55%, Intra-stream: 45% averaged over 52 frames drawn from twelve DirectX apps
Inter-stream reuses
  Out of all LLC blocks with the RT bit set, 51% are consumed by the texture samplers in Belady’s optimal policy
  DRRIP and NRU: 16%, 13%
  With Belady’s optimal policy, each of the twelve applications has at least one-third RT blocks consumed by the texture samplers

## Slide 16: LLC reuse study#1: Texture
Inter-stream reuse: take-away
  Retaining RT blocks in the LLC is important for improving texture sampler throughput
  Without driver assistance, it is difficult to identify the render targets that will be used as textures
  In this work, we consider all render targets to be potential source for dynamic textures and refine this set based on render to texture reuse probability learned at run-time
Why DRRIP falls so much short of optimal
  Fills 25% of the RT blocks with RRPV three
  Level of protection for RT fills must be decided from the render to texture reuse probability

## Slide 17: LLC reuse study#1: Texture
Intra-stream reuses
  The goal is to understand how a dead texture block in the LLC can be identified and evicted creating room for other live graphics data
  Divide the life of a texture block in the LLC into epochs demarcated by hits
Time
E0
Sampler access misses LLC and fills a texture block B OR sampler consumes an RT block B
E1
E2
E3
Sampler access hits block B in LLC
LLC evicts block B
Intra-stream reuses

## Slide 18: LLC reuse study#1: Texture
Intra-stream reuses
  All texture blocks residing in the LLC at any point in time can be partitioned into disjoint sets based on their epochs
  Clearly, the set Ek+1 is a subset of the set Ek for all k≥0
  Define death ratio of epoch Ek as (|Ek| – |Ek+1|)/|Ek|
  Define reuse probability of epoch Ek as |Ek+1|/|Ek|
  Goal of a good policy should be to attach a high victimization priority to the epochs with low reuse probability

## Slide 19: LLC reuse study#1: Texture
How many epochs are statistically significant
  When the LLC runs Belady’s optimal policy, 79% of all texture sampler hits come from the E0 epoch, 15% from the E1 epoch, 4% from the E2 epoch, and 2% from the E≥3 epoch
  It is enough to keep track of the E0, E1, and E≥2 epochs for a texture block
Average reuse probability of these epochs
  E0: 0.19 (at most 0.3 across the twelve apps)
  E1: 0.27 (varies a lot across applications: 0.6 to nearly zero)
  E2: 0.47 (can be assumed to be mostly live)

## Slide 20: LLC reuse study#1: Texture
Intra-stream reuse: take-away
  Need to track the epoch membership of a texture block (one among E0, E1, E≥2)
  Need to learn the reuse probabilities of the E0 and E1 epochs dynamically
  Texture blocks entering the E≥2 epoch will be assumed to be live unconditionally
Why DRRIP falls so much short of optimal
  DRRIP fills slightly over a third of the texture blocks with RRPV three in the LLC
  Need to eliminate more dead texture blocks
  Cannot always promote to RRPV zero on hit

## Slide 21: LLC reuse study#2: Depth
Only intra-stream reuses from the LLC
  Generated depth buffer values are consumed for further depth tests
  Use the same epoch-based formalism
Reuse probabilities of the first three epochs
  E0: 0.39, E1: 0.62, E2: 0.74
  Very different from the texture epochs
  Only the E0 blocks have low reuse probability and the E≥1 blocks are practically live
  We will decide the insertion RRPV of the Z blocks by estimating the aggregate reuse probability of all Z blocks and won’t consider epochs

## Slide 22: LLC reuse: Render target
Render targets source two types of LLC hits
  Texture sampler hits for render to texture
  Render target blending (also known as texture blending), where an already created render target is blended with another render target being created currently (transparency modeling)
We do not implement any policy for improving render target blending
  DRRIP is within 10% of optimal in hit rate
  Some of the lost LLC hits in blending operations can be recovered by eliminating dead textures
  Our render target hit rates are close to optimal

## Slide 23: Sketch
Talk in one slide
Result highlights
Understanding the potential
Reuses in 3D graphics data
Our policy proposals
Evaluation methodology
Simulation results
Summary

## Slide 24: Graphics stream-aware policies
Basic framework
  LLC accesses are partitioned into four streams based on the source: texture samplers (TEX), render targets (RT), depth (Z), and the rest
  All policies modulate the two-bit RRPV of an LLC block on insertion and promotion based on reuse probabilities
    A larger RRPV corresponds to a smaller probability of reuse; the blocks with RRPV three are potential victim candidates
  The reuse probabilities are estimated by maintaining fill and hit counters for a few sampled LLC sets that always use SRRIP [ISCA’10]

## Slide 25: Graphics stream-aware policies
Policy#1: Graphics stream-aware probabilistic Z and texture caching (GSPZTC)
SRRIP samples
FILL(Z)
HIT(Z)
Inc. on Z fills to samples
Inc. on RT to TEX and TEX fills to samples
Inc. on Z hits to samples
FILL(TEX)
HIT(TEX)
LLC
Sets

## Slide 26: Graphics stream-aware policies
GSPZTC policy for non-sample sets
  The insertion RRPV of a block depends on the reuse probability of the stream it belongs to
  Z fill: RRPV ← (FILL(Z) > t.HIT(Z)) ? 3:2
  The reuse probability threshold of 1/(t+1) is determined empirically; we use t=8
  TEX fill: RRPV ← (FILL(TEX) > t.HIT(TEX)) ? 3:0
  RT fill: RRPV ← 0 (highest protection)
  All other fills: RRPV ← 2 (like SRRIP)
  All hits: RRPV ← 0 (like any RRIP)
  Each LLC block has an RT bit to identify RT to TEX reuse

## Slide 27: Graphics stream-aware policies
Policy#2: GSPZTC with texture sampler epochs (GSPZTC+TSE)
  Each LLC block has two state bits to keep track of E0, E1, and E≥2 epochs for texture blocks; the fourth state serves the functionality of the RT bit
  The FILL(TEX) and HIT(TEX) counters are replaced by FILL(E0, TEX), FILL(E1, TEX), HIT(E0, TEX), and HIT(E1, TEX)
  Recall: enough to estimate the reuse probabilities of the E0 and E1 epochs
  Recall: the E≥2 blocks are unconditionally live (assumed to have high reuse probability)

## Slide 28: Graphics stream-aware policies
Policy#2: GSPZTC with texture sampler epochs (GSPZTC+TSE)
E0
E1
E≥2
Sampler access misses LLC and fills a texture block B OR sampler consumes an RT block B
Texture reuse
Texture reuse
Texture reuse
FILL(E0, TEX)++
HIT(E0, TEX)++
FILL(E1, TEX)++
HIT(E1, TEX)++

## Slide 29: Graphics stream-aware policies
Policy#2: GSPZTC+TSE for non-sample sets
  TEX fill or RT to TEX reuse: RRPV ← (FILL(E0, TEX) > t.HIT(E0, TEX)) ? 3:0
  TEX hit to a block in epoch E0: RRPV ← (FILL(E1, TEX) > t.HIT(E1, TEX)) ? 3:0
  TEX hit to a block in epoch E1: RRPV ← 0
  Other rules are same as GSPZTC
  Observe that both GSPZTC and GSPZTC+TSE offer the highest protection to the newly filled render target blocks
    Unnecessarily wastes cache space if the likelihood of RT to TEX reuse is low
    The next policy addresses this problem

## Slide 30: Graphics stream-aware policies
Policy#3: GSPZTC+TSE + RT insertion policy
  Our final proposal: graphics stream-aware probabilistic caching (GSPC)
  Incorporates two new counters PROD and CONS
  PROD is incremented on an RT fill to a sample set; left untouched on RT blending hits
    Approximately tracks the number of unique RT blocks mapping to the sample sets
  CONS is incremented on RT to TEX reuses in the sample sets
    One increment for every consumed RT block
    The block enters the E0 state after this
  Inter-stream reuse probability is CONS/PROD

## Slide 31: Graphics stream-aware policies
Policy#3: GSPC for non-sample sets
  RT fill: If PROD > 16.CONS then RRPV ← 3
  [[Low inter-stream reuse probability]]
  Else if 16.CONS ≥ PROD > 8.CONS then
  RRPV ← 2
  [[Medium inter-stream reuse probability]]
  Else RRPV ← 0
  [[High inter-stream reuse probability]]
  RT hit (blending): RRPV ← 0
  RT to TEX reuse: as in GSPZTC+TSE
  All other rules are same as GSPZTC+TSE

## Slide 32: Graphics stream-aware policies
Hardware overhead of GSPC on top of two RRPV bits per LLC block
  Two new state bits per LLC block
  Eight short counters per LLC bank: reuse probabilities are de-centralized and maintained per bank to avoid counter hotspots
    HIT(Z), FILL(Z), HIT(E0, TEX), FILL(E0, TEX), HIT(E1, TEX), FILL(E1, TEX), PROD, CONS: eight bits each
    A seven-bit counter to maintain the interval at which the above counters are halved: probabilities are computed on exponentially averaged estimates
  Overall, less than 0.5% of all LLC data bits

## Slide 33: Sketch
Talk in one slide
Result highlights
Understanding the potential
Reuses in 3D graphics data
Our policy proposals
Evaluation methodology
Simulation results
Summary

## Slide 34: Evaluation methodology
Detailed timing model of a high-end GPU
  Eight thread contexts per shader core
    Two threads can issue one four-wide vector operation (including MAD) each per cycle
  One texture sampler for every eight shader cores
  Two configs: 64 and 96 shader cores @ 1.6 GHz
    Peak shader throughput: 1.6 TFLOPS and 2.5 TFLOPS
    512 and 768 thread contexts
  LLC configs: 8 MB and 16 MB 16-way 4 GHz
    2 MB per bank, non-inclusive/non-exclusive
  DRAM configs: Dual-channel DDR3-1600 15-15-15 8-way banked
52 frames from twelve DirectX applications

## Slide 35: Sketch
Talk in one slide
Result highlights
Understanding the potential
Reuses in 3D graphics data
Our policy proposals
Evaluation methodology
Simulation results
Summary

## Slide 36: Total volume of LLC misses
Config: 768 shader contexts, 12 texture samplers, 8 MB LLC
0.80
0.84
0.88
0.92
0.96
1.00
1.04
1.08
DRRIP
NRU
SHiP-mem
GS-DRRIP
GSPZTC
GSPZTC+TSE
GSPC
GSPC+UCD
DRRIP+UCD
1.06
1.00
0.97
0.95
0.89
0.88
0.87
1.00
The best policy proposal saves 13% LLC misses on average (1.7% to 29.6%)

## Slide 37: RT to TEX reuse through LLC
Config: 768 shader contexts, 12 texture samplers, 8 MB LLC
10%
15%
20%
25%
30%
35%
40%
45%
NRU
SHiP-mem
GS-DRRIP
GSPZTC
GSPZTC+TSE
GSPC
GSPC+UCD
DRRIP+UCD
13.1%
14.6%
20.0%
42.3%
38.7%
40.4%
16.6%
16.3%
DRRIP
30.4%
RT to TEX reuse through LLC offered by the best proposal is close to optimal (51%)

## Slide 38: LLC hit rate: Texture sampler
Config: 768 shader contexts, 12 texture samplers, 8 MB LLC
15%
18%
21%
24%
27%
30%
33%
36%
NRU
SHiP-mem
GS-DRRIP
GSPZTC
GSPZTC+TSE
GSPC
GSPC+UCD
DRRIP+UCD
18.4%
21.5%
23.8%
33.3%
32.2%
33.5%
22.2%
22.0%
DRRIP
27.8%
The best proposal still lags significantly behind the optimal (53.4%)

## Slide 39: LLC hit rate: RT accesses
Config: 768 shader contexts, 12 texture samplers, 8 MB LLC
36%
40%
44%
48%
52%
56%
60%
NRU
SHiP-mem
GS-DRRIP
GSPZTC
GSPZTC+TSE
GSPC
GSPC+UCD
DRRIP+UCD
41.5%
49.3%
51.1%
57.7%
58.3%
50.0%
50.1%
DRRIP
50.8%
The best proposal offers nearly optimal (59.8%) RT hit rate
53.1%

## Slide 40: Frame rate improvement
Config: 768 shader contexts, 12 texture samplers, 8 MB LLC, DDR3-1600 15-15-15
Config: All identical except 16 MB LLC
0.90
0.94
0.98
1.02
1.06
1.10
1.14
NRU+UCD
GS-DRRIP+UCD
GSPC+UCD
DRRIP+UCD
1.01
0.93
1.08
0.90
0.94
0.98
1.02
1.06
1.10
1.14
NRU+UCD
GS-DRRIP+UCD
GSPC+UCD
1.04
0.97
1.12
DRRIP+UCD
Frame rate improvements in GSPC gracefully scale with LLC capacity

## Slide 41: Sensitivity to shader thread count
Config: 768 shader contexts, 12 texture samplers, 8 MB LLC, DDR3-1600 15-15-15
Config: All identical except 512 shader contexts
0.90
0.94
0.98
1.02
1.06
1.10
1.14
NRU+UCD
GSPC+UCD
DRRIP+UCD
0.93
1.08
0.90
0.94
0.98
1.02
1.06
1.10
1.14
NRU+UCD
GSPC+UCD
0.95
1.06
DRRIP+UCD
Our proposal gains in importance as the GPU puts more pressure on the memory system with more threads

## Slide 42: Sketch
Talk in one slide
Result highlights
Understanding the potential
Reuses in 3D graphics data
Our policy proposals
Evaluation methodology
Simulation results
Summary

## Slide 43: Summary
Graphics processor’s LLC is shared by different data structures used in 3D scene rendering applications
Render targets (same as pixel colors), textures, and depth buffer contribute most to the LLC access traffic
We propose reuse probability-based algorithms to efficiently manage the GPU LLC
Our best proposal saves 13.1% LLC misses and speeds up rendering by 8% on average in a GPU with an 8 MB LLC
Speedup improves to 11.8% for a 16 MB LLC

## Slide 44: Where do we lose against optimal
Render target to texture reuse
  Optimal: 51%, GSPC+UCD: 40.4%
Render target blending hit rate
  Optimal: 59.8%, GSPC+UCD: 58.1%
Texture sampler hit rate
  Optimal: 53.4%, GSPC+UCD: 33.5%
Z hit rate
  Optimal: 77.1%, GSPC+UCD: 59%
Need a better model for intra-stream texture and Z reuses that can construct partitions more useful than reuse count-based epochs
About 10%
About 2%
About 20%
About 18%

## Slide 45
Thank you
Nothing clears up a case so much
as stating it to another person.
-Sir Arthur Conan Doyle
[Silver Blaze (1892)]